Creating debug configuration in NuEclipse.
Go to Eclipse menu->Run->”Debug Configuration”

Right click on “GDB Nuvoton Nu-Link Debugging” and select ‘New’.

Main tab:
1. Select some name for configuration.
2. In ‘Project field press ‘Browse...’ and select the project you want to debug.
3. In “C/C++ Application” put path to the output .elf file of you compilation. Usually the output located in $(YOUR_APP)/zOUT/ folder.
Debugger tab:

1. Select ‘Start OpenOCD Localy’
2. In OpenOCD ‘Executable:’ make sure that path points to openocd.exe executable.
3. GDB port : 3333
4. Telent por: 4444
5. Config options:
  select proper configuration based on your target SOC:
  M4 : -f ../scripts/interface/nulink.cfg -f ../scripts/target/numicroM4.cfg
  M0 : -f ../scripts/interface/nulink.cfg -f ../scripts/target/numicroM0.cfg

In GDB Client Setup
a. Executable: IMPORTANT! You have to select gdb from compiler package that you used to compile the project.
b. Commands: set mem inaccessible-by-default off
Startup tab

1. in Chip series:
  For M4 – select NuMicro M4
  For M0 – select NuMicro M0
2. Check ‘Load Symbols and Executable’ and select ‘Use project binary. ...’
3. Un-check ‘Load executable to flash’
4. Un-check ‘Load executable to SRAM’